## Slide 1
What should we expect
before we simulate?
Order-of-magnitude physics of a 1.4 m plastic scintillator bar for the SHiP Timing Detector — energy deposition, total internal reflection, photon transport, reflector losses and timing observables, derived before any Geant4 output is shown.
René Ríos
Universidad de La Serena · SHiP Timing Detector · August 2026
Napkin first. Geant4 second.
Notes: Idea rectora: la simulacion no puede reemplazar el entendimiento.

## Slide 2
THE OBJECT
One bar is a cell of a 50 m² detector
TOP · up to 70 SiPM along the bar
END · 8 SiPM per face
1400 mm × 60 mm × 10 mm
0.084 m²
geometric area of one bar
~600
bars needed for a 50 m² detector
9.6k – 50k+
SiPM in total, for 16 / 70 / 86 per bar
DESIGN QUESTION
Which combination of optical transport, SiPM number and position, and time estimator gives the best resolution per readout channel — knowing that every bar is one small cell of an almost 50 m² surface?
BEST TESTED SO FAR — NOT A PROVEN OPTIMUM
EJ-230 + END + Vikuiti with air gap:
σ(T0) ≈ 58.6 ps, σx ≈ 10.3 mm, veff ≈ 184.6 mm/ns, Npe ≈ 1400 at the centre (no electronic jitter).
A small loss in resolution against a large reduction in channels may be globally preferable.
SHiP Timing Detector · 1.4 m scintillator bar · first principles before Geant4
2
Notes: 600 barras. La resolucion por canal es la metrica relevante.

## Slide 3
The simulation must not cover our understanding
Geant4 returns a number. Only a prior analytic estimate tells us whether that number is physics or a bug.
1 — NAPKIN
Snell, geometry, exponential attenuation and order statistics fix the order of magnitude and, more importantly, the direction of every trend: which material gives more light, which gives better timing, which face imposes more bounces.
2 — GEANT4
Confirms the scale, adds the distributions the napkin cannot produce — Landau fluctuations, path-length dispersion, angular mixing — and quantifies what we already expected qualitatively.
Knoll, Ch. 8, on optical Monte Carlo: these codes are accurate only to the extent that the assumptions about surface reflection, bulk absorption and the refractive indices of every medium are correct. Those are exactly the three inputs a napkin calculation can police.
If the two disagree, one of them is wrong — and finding out which one is the actual result.
Notes: Knoll lista las tres suposiciones del Monte Carlo optico: superficies, absorcion, indices.

## Slide 4
1
STEP 1 — ENERGY DEPOSITION
How much energy does one muon leave?
dE/dx ≈ 2 MeV/cm (minimum ionizing, plastic)
T = 10 mm → Edep ≈ 2 MeV
≈ 2 MeV
deposited in 10 mm of scintillator
One number, one line of arithmetic — but it sets the scale of everything downstream.
It is deliberately crude: it fixes an order of magnitude, not a distribution.
Every later factor in this talk multiplies this 2 MeV.
WHAT THE NAPKIN CANNOT GIVE
Geant4 adds the event-by-event fluctuation: full Bethe–Bloch, Landau tail, δ-ray production. The mean survives; the width is simulation territory.
SHiP Timing Detector · 1.4 m scintillator bar · first principles before Geant4
4
Notes: 2 MeV/cm fija escala. Geant4 aporta la distribucion Landau.

## Slide 5
2
STEP 2 — SCINTILLATION YIELD
From 2 MeV to twenty thousand photons
Nγ = Edep · Y ≈ 2 × 9700 ≈ 1.94 × 10⁴ photons
≈ 2 × 10⁴
optical photons per crossing muon
Optical properties used in the simulations
Material | Yield [ph/MeV] | τd [ns] | λatt [cm]
EJ-200 | 10000 | 2.1 | 380
EJ-204 | 10400 | 1.8 | 160
EJ-230 | 9700 | 1.5 | 120
THE TRADE-OFF IS ALREADY VISIBLE
The three yields are the same to within 7 %. What separates the materials is not how much light they make, but how much survives 70 cm of travel (λatt) and how fast the emission decays (τd). Those two pull in opposite directions.
SHiP Timing Detector · 1.4 m scintillator bar · first principles before Geant4
5
Notes: El yield no discrimina: difiere 7%. Discriminan lambda_att y tau_d.

## Slide 6
3
STEP 3 — TOTAL INTERNAL REFLECTION
How much of that light can stay inside?
ns sin θc = na , ns ≈ 1.58 → θc = 39.3°
αc = 90° − θc = 50.7° measured from the surface
|u⊥| < cos θc = √(1 − 1/ns²) = 0.774
An exact trigonometric identity combined with Snell — no Taylor expansion, no small-angle approximation.
isotropic: P(|uy| < a) = a = 0.774 per wall family
both transverse dimensions: fTIR = 2a − 1 ≈ 0.548
KNOLL EQ. 8.15 — SLAB GEOMETRY
F = √(1 − (n1/n0)²) = cos θc. The textbook quotes 75 % at n = 1.5; at n = 1.58 it returns 0.774 — our single wall family, exactly.
BUT THE BAR IS NOT A SLAB
Two wall families must hold simultaneously: fTIR = 2a − 1 = 0.548, i.e. ≈ 0.274 towards each end. That split matters later.
AND IT IS NOT A CYLINDER EITHER
Knoll Eq. 8.14, meridional rays: ½(1 − n1/n0) = 18.4 % per direction. A different geometrical quantity from the 80 % quoted for EJ-228 — not comparable as it stands.
SHiP Timing Detector · 1.4 m scintillator bar · first principles before Geant4 | Knoll, Radiation Detection and Measurement, Ch. 8, Eqs. 8.14–8.15
6
Notes: Nuestro 0.774 ES la Ec. 8.15 de Knoll para slab: la servilleta contiene al libro como caso limite y lo extiende a dos familias de paredes. Sobre el 80% del cilindro: NO afirmar que este mal, sino que define otra cantidad geometrica. Knoll ademas advierte que 8.14 cuenta solo rayos meridionales.

## Slide 7
4
STEP 4 — LONGITUDINAL VELOCITY
How fast does the light travel — and how axial is it?
vg ≈ c/ns ≈ 190 mm/ns → 700 mm in ≈ 3.7 ns (axial ray)
vx = (c/ns) cos β → diagonal rays are longitudinally slower
Reading Geant4 backwards: what equivalent angle does the measured propagation slope imply?
END: cos βeff = 184.6 / 189.9 → βeff ≈ 13.5°
TOP: veff ≈ 145 mm/ns → βeff ≈ 40°
KEY IDEA
END and TOP do not merely read the light in different places — they select different angular families of photons. END is dominated by an almost axial, early population; TOP integrates markedly more diagonal trajectories.
READ ΒEFF AS A SLOPE, NOT AS A BEAM
veff is a statistical slope built from the earliest photons, so βeff is the equivalent axial angle of that slope — not evidence of a mono-angular population. Knoll also notes that adding escape surfaces lowers the mean number of reflections.
SHiP Timing Detector · 1.4 m scintillator bar · first principles before Geant4 | Knoll Ch. 8 on multiple readout surfaces
7
Notes: Importante: beta_eff es angulo EQUIVALENTE asociado a la pendiente de propagacion. No hemos demostrado una poblacion monoangular a 13.5 grados. Esto evita una pregunta incomoda de alguien de optica.

## Slide 8
5
STEP 5 — BOUNCE COUNTING
Geometry, not the reflector, sets the number of bounces
Nbounce ≈ d · tan β / D (geometric estimate)
2D limiting case, for a ray just outside TIR on that wall family: β ≈ 50.7° → tan β ≈ 1.22, travelling d = 700 mm from the centre.
D = 10 mm
≈ 85
bounces, thin face
D = 60 mm
≈ 14
bounces, wide face
THE TWO TRANSVERSE DIMENSIONS ARE NOT EQUIVALENT
A 1400 × 60 × 10 mm bar is thin in one direction and wide in the other. The same photon direction produces six times more reflections against the 10 mm face than against the 60 mm face.
Ny ≈ d|uy| / (W|ux|)
Nz ≈ d|uz| / (T|ux|)
The 3D form is the rigorous one: the integer bounce count also depends on where in the cross-section the photon starts.
SHiP Timing Detector · 1.4 m scintillator bar · first principles before Geant4
8
Notes: No decir exacto: la geometria del triangulo lo es, el numero entero de impactos no. En 3D el angulo total respecto de x no es lo mismo que u_y y u_z por separado.

## Slide 9
6
STEP 6 — REFLECTOR LOSSES
A 2 % loss per bounce becomes an exponential attenuation
PR = R^N = exp(N ln R), N ≈ d tan β / D
PR(d) = exp(−d / Λrefl), Λrefl = − D / (tan β · ln R)
Λrefl (β = 50.7°)
≈ 0.4 m
10 mm face
Λrefl (β = 50.7°)
≈ 2.4 m
60 mm face
These are not attenuation lengths of Vikuiti. Reflector attenuation is reflectivity × geometry × photon direction, and both numbers are conditioned on the angle chosen above.
Chart: Survival vs number of reflections N (R = 0.98)
| 0 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100
Survival R^N, R = 0.98 | 1 | 0.817 | 0.668 | 0.545 | 0.446 | 0.364 | 0.298 | 0.243 | 0.199 | 0.162 | 0.133
0.98¹ = 0.98 · 0.98¹⁰ = 0.82 · 0.98⁵⁰ = 0.36 · 0.98¹⁰⁰ = 0.13
SHiP Timing Detector · 1.4 m scintillator bar · first principles before Geant4
9
Notes: El eje horizontal va de 0 a 100 en pasos de 10, NO de 1 a 11. La linea de valores debajo del grafico lo hace explicito.

## Slide 10
7
STEP 7 — MATERIAL CHOICE
Bulk attenuation and decay time pull in opposite directions
s = d / |ux| → Pbulk(ux) = exp( − d / (λatt |ux|) )
The familiar exp(−70/λatt) at the bar centre is the axial best case, |ux| = 1. Every diagonal ray travels further and survives less.
Chart: Axial best case, centre to one end
| EJ-200 (380 cm) | EJ-204 (160 cm) | EJ-230 (120 cm)
Light surviving 70 cm | 0.83 | 0.65 | 0.56
NAPKIN PREDICTION, MADE BEFORE THE RUN
EJ-200 must deliver the most light to the ends (largest λatt).
EJ-230 must lose the most light, but its faster kinetics (τd = 1.5 ns vs 2.1 ns) should win on timing.
GEANT4
Npe: EJ-200 > EJ-204 > EJ-230
σt: EJ-230 < EJ-204 < EJ-200
Both orderings reproduced, in the predicted directions — the curves are on the next slide.
SHiP Timing Detector · 1.4 m scintillator bar · first principles before Geant4
10
Notes: Conectar con slides 7 y 9: la distancia optica real es d/|ux|, no d.

## Slide 11
PREDICTIVE VALIDATION
The ordering was predicted, then measured
Npe(x) · EJ-200 / EJ-204 / EJ-230
Insert the light-yield-versus-position curves from the END + Vikuiti campaign. The napkin predicts the ordering EJ-200 > EJ-204 > EJ-230 at every x, and a steeper fall for the shorter λatt.
σ(T0)(x) · EJ-200 / EJ-204 / EJ-230
Insert the timing-resolution-versus-position curves from the same campaign. The napkin predicts the opposite ordering, EJ-230 < EJ-204 < EJ-200, driven by τd.
Two figures, two orderings, opposite directions — both written down before the Monte Carlo was run. This is the difference between illustrating a simulation and validating a prediction.
SHiP Timing Detector · 1.4 m scintillator bar · first principles before Geant4
11
Notes: ACCION REQUERIDA: reemplazar los dos marcos punteados por las figuras reales Npe(x) y sigma(T0)(x) de las campanas EXEC, con sus sidecars .csv/.meta.json. Esta slide convierte la charla de derivacion analitica en validacion predictiva.

## Slide 12
CLOSING THE CHAIN
Photon budget: multiply the factors and check the scale
1.94 × 10⁴
photons produced
× 0.274
TIR-guided towards ONE end (0.548 / 2)
× 0.56
bulk attenuation, 70 cm
× 0.48
end coverage, 288 / 600 mm²
≈ 1.4 × 10³
photons at that end
× PDE ≈ 0.4 → ≈ 5.7 × 10² PE per end ≈ 1.1 × 10³ for L + R
Geant4, EJ-230 + END + Vikuiti at the centre: Npe ≈ 1400. The chain closes, and the excess is what the reflector-recovered population should add.
The factors are not strictly independent (coverage, PDE, incidence angle and multiple chances to hit a sensor are correlated). This is a scale check, not a prediction.
COUNT PER END, ALWAYS
Half the guided population goes each way. Mixing a both-ends fraction with a one-end coverage silently doubles the answer.
THE OUTSTANDING ANOMALY
A historical END + TIR-only run returned of order 1 PE per event. Before that is called physics, it has to survive the most pessimistic napkin we can write.
SHiP Timing Detector · 1.4 m scintillator bar · first principles before Geant4
12
Notes: CORRECCION respecto de la version anterior: la fraccion TIR 0.548 cuenta ambas direcciones; con cobertura de UN extremo hay que usar 0.274. Asi el presupuesto da 1.1e3 PE (L+R) contra 1400 de Geant4, mejor acuerdo que antes. Confirmar en datasets.py si Npe=1400 es L+R o por extremo.

## Slide 13
AUDITING THE 1 PE RUN
Even the worst case leaves two orders of magnitude
Readout-face treatment | Angular acceptance towards one end | PE per end | Implied Vikuiti / TIR-only
Index-matched coupling | 0.274 (TIR-guided) | ≈ 5.7 × 10² | ≈ 1.2
Air gap, escape cone only | 0.113 = (1 − 0.774) / 2 | ≈ 2.4 × 10² | ≈ 3
Reported run | — | ≈ 1 PE / event | ≈ 10³
THE ESCAPE CONE CANNOT BE THE EXPLANATION
Knoll warns that TIR must be minimised on the face you read from. But that cone sits at the readout face, so it cuts the Vikuiti configuration by the same factor — it cannot generate a ratio.
The only genuine difference is the side walls: 0.548 guided, versus 0.548 plus whatever the reflector recovers.
THE FALSIFIABLE PREDICTION
Run END + TIR-only and END + Vikuiti under identical conditions and compare per-end yields. The napkin brackets the ratio between roughly 1 and 3 — every other factor cancels.
A ratio near 10³ is not a physical result. It is a surface, boundary or RINDEX definition to be found.
SHiP Timing Detector · 1.4 m scintillator bar · first principles before Geant4 | Knoll Ch. 8 on the readout face and index-matched coupling
13
Notes: Reformulado: el cono de escape actua en la cara de lectura y por tanto afecta IGUAL a Vikuiti. No puede generar un cociente. La unica diferencia real entre configuraciones son las paredes laterales. Cociente predicho 1-3, no 6. Comparar SIEMPRE por extremo.

## Slide 14
THE MEASUREMENT
From arrival times to physical observables
tL = t0 + (L/2 + x)/veff + εL
tR = t0 + (L/2 − x)/veff + εR
SUM
T0 = (tL + tR)/2
x cancels → vertex time
DIFFERENCE
Δt = tR − tL = −2x/veff
→ longitudinal position
σx = (veff / 2) · σΔt
CONSISTENCY CHECK, NOT AN EXTRA MEASUREMENT
veff = 184.6 mm/ns and σΔt = 111.5 ps give
σx = 92.3 × 0.1115 ≈ 10.3 mm,
exactly what the simulation reports. The position resolution is not independent information — it is the timing resolution seen through the propagation velocity.
DECOMPOSITION OF THE MEASURED TIME
tmeas = t0 + tscint + tprop + tsensor + telec
tprop is a distribution of path lengths, not a constant. Knoll flags exactly this case: for fast emitters of large dimensions, the spread in photon path lengths can limit the achievable timing resolution.
SHiP Timing Detector · 1.4 m scintillator bar · first principles before Geant4 | Knoll Ch. 8 on path-length spread in large, fast scintillators
14
Notes: sigma_x no es informacion nueva: es sigma_dt propagada por veff.

## Slide 15
SCOREBOARD
Napkin versus Geant4 and the literature
Quantity | Napkin prediction | Geant4 / literature | Verdict
Photons per muon | ≈ 2 × 10⁴ | same order | consistent
Trapped fraction, one wall family | 0.774 | Knoll Eq. 8.15: 0.774 | textbook match
Longitudinal velocity | ≤ 190 mm/ns, axial limit | 184.6 mm/ns → βeff ≈ 13.5° | consistent
Npe at centre, END + Vikuiti | ≈ 1.1 × 10³ (L + R) | ≈ 1400 | consistent
Light ordering | EJ-200 > EJ-204 > EJ-230 | same ordering | confirmed
Timing ordering | EJ-230 < EJ-204 < EJ-200 | same ordering | confirmed
σx from σΔt | 10.3 mm | 10.3 mm | internal check
Cylinder trapping (EJ-228) | 18.4 % per direction (Eq. 8.14) | 80 % quoted | different definition — check
Vikuiti / TIR-only yield ratio | between 1 and 3 | ≈ 10³ | AUDIT THE RUN
Seven agreements. One quantity that needs its definition checked. One genuine anomaly.
SHiP Timing Detector · 1.4 m scintillator bar · first principles before Geant4
15
Notes: El cilindro pasa de 'figure suspect' a 'definicion distinta, verificar'. Mas seguro y cientificamente mas fuerte.

## Slide 16
THE CONCEPTUAL CENTRE OF THE TALK
Two photon populations, two kinds of information
A — TIR-guided: large |ux|, few bounces, vx close to c/n, first to arrive
B — reflector-recovered: large transverse component, many bounces, R^N penalty, arrives late
END
WHAT THE REFLECTOR BUYS
A large increase in total collected light, concentrated in the late part of the arrival distribution.
WHAT IT DOES NOT BUY
A proportional improvement in the statistics of the earliest photons, which is what a leading-edge estimator uses.
Total Npe ≠ timing information carried by the first photons
SHiP Timing Detector · 1.4 m scintillator bar · first principles before Geant4
16
Notes: Esta es la idea fisica central de toda la charla. Dos rayos, dos historias temporales. Frase de cierre: Npe total no es lo mismo que informacion temporal en los primeros fotones.

## Slide 17
A CAMPAIGN WE HAVE NOT RUN
Specular or diffuse? The napkin gives us a falsifiable prediction
SPECULAR — VIKUITI 3M ESR
Preserves the angle of incidence, so a photon outside the acceptance of the readout face is never redirected into it.
It also preserves short paths, keeping the dispersion of tprop small.
DIFFUSE — TEFLON, TIO₂, MGO
Lambert's law, dI/dΩ ∝ cos ψ: the outgoing direction is essentially independent of the incoming one.
Every bounce is a fresh chance to be redirected towards a readout window, at the cost of a broader path-length distribution.
Napkin hypothesis: at comparable reflectivity, diffuse scattering should raise the probability of redirecting photons into a readout window, and should broaden tprop. One campaign, one variable, prediction on record.
Stated as a hypothesis, not a conclusion: a real diffuse wrapping differs from a specular one in spectral reflectivity, absorption and surface finish, not only in angular law. Knoll reports diffuse reflectors generally collect light better — but that comparison is made on light yield, not on timing. Kilvington's data (Knoll Fig. 8.17) show TIR with a reflective covering sitting systematically above TIR alone, both falling with guide length.
SHiP Timing Detector · 1.4 m scintillator bar · first principles before Geant4 | Knoll Eq. 8.13 and Fig. 8.17 (Kilvington et al.)
17
Notes: Tono: hipotesis falsable, no respuesta ya conocida. Knoll compara especular vs difuso en colecicion de luz, no en timing; nosotros optimizamos timing.

## Slide 18
THE OPEN QUESTION
Why assume the first photon is optimal?
T0⁽¹⁾ = ( tL⁽¹⁾ + tR⁽¹⁾ ) / 2 → σ ≈ 58.6 ps
EVIDENCE THAT K = 1 NEED NOT BE THE OPTIMUM
In an independent EJ-228 cylinder study σ(k) is non-monotonic, with an optimum near k ≈ 8. The number does not transfer to a 1.4 m bar — the principle does.
How much timing information are we throwing away by using only t⁽¹⁾ ?
ORDER STATISTICS
t⁽ᵏ⁾ for k = 1 … 100; fractional rank k ≈ f · Npe
MULTI-PHOTON ESTIMATORS
mean / median / trimmed mean of the first m; Σ wi ti; accumulated-PE threshold; digital CFD; temporal template
MULTI-READOUT ESTIMATORS
BLUE(L, R) instead of a plain average; END + TOP through the residual covariance
σoptical → SiPM SPTR → front-end → clock / common mode. 58.6 ps is the optical limit alone: if SPTR is of order 100 ps, winning 14 ps optically may matter less than halving the channel count.
SHiP Timing Detector · 1.4 m scintillator bar · first principles before Geant4
18
Notes: Tres familias, no nueve items. La banda de electronica conecta con la pregunta de diseno de la slide 2: si SPTR domina, conviene recortar canales antes que perseguir ps opticos.

## Slide 19
PROGRAMME
What the napkin tells us to do next
A
Exploit the existing data first
Audit the ROOT files for arrival time, SiPM ID, face, PE, wavelength and true muon position — and fix the per-end versus L+R convention before any ratio is quoted.
B
Close the 1 PE question with a ratio
Re-run END + TIR-only and END + Vikuiti under identical conditions. The napkin brackets the per-end yield ratio between 1 and 3; anything near 10³ is a surface or RINDEX definition problem.
C
Separate the two ablations
Masking a channel offline is not the same as removing the sensor from the geometry: physical removal changes the optical boundary condition and therefore the transport.
D
Report a Pareto front, not a minimum
σt (mean and worst case in x) against the number of channels, with SPTR and front-end jitter injected. Quadrature does not automatically apply to multi-channel estimators.
SHiP Timing Detector · 1.4 m scintillator bar · first principles before Geant4
19
Notes: El punto A ahora incluye fijar la convencion por extremo vs L+R, que es lo que casi nos hace citar un cociente equivocado.

## Slide 20
Three messages
1
Geometry explains the scale.
TIR, propagation and repeated reflection already predict the dominant trends — and reproduce the textbook where the textbook applies.
2
More light is not necessarily better timing.
Early TIR photons and late reflector-recovered photons carry different information. Total Npe is the wrong figure of merit for a timing detector.
3
The optimisation problem is still open.
The optimum is not the maximum number of SiPM. It is the Pareto optimum of σt against the number of channels, once SPTR and front-end jitter are in.
EJ-230 + END + Vikuiti is the best tested point — not yet the optimum.
Notes: Cierre en tres mensajes. La frase final resume la postura cautelosa por diseno.